## Slide 1
END-TO-END SOLUTIONS
High Pressure Water Jetting
Basic Operator Training
(Awareness & Field Verification)
Day 1 – Safety Foundation, Hazards, Medical Response & Controls
Anabeeb HSE & Training | NEBOSH Verified Programme

## Slide 2: HPWJ – WATER JETTING
This programme is delivered to NEBOSH Verified standards.
It follows industry best practices and international standards for high pressure water jetting operations.
You will receive an Anabeeb certificate and personal Medical Alert Card upon successful completion of the full 3-day programme and assessments.
The NEBOSH Verified logo signifies training quality that meets recognised standards.
This training enhances safety during shutdown and turnaround operations on oil and gas sites.
NEBOSH VERIFIED PROGRAMME

## Slide 3: HPWJ – WATER JETTING
By the end of today you will be able to:
Understand why high pressure water jetting injuries are different and serious
Explain the Medical Alert Card and when to use it
Apply the hierarchy of controls and key site safety rules
Understand how the system creates pressure and why control of relief is critical
Recognise Stop Work Authority and when to use it
DAY 1 LEARNING OUTCOMES

## Slide 4: HPWJ – WATER JETTING
This session is interactive, not just a lecture
You are welcome to ask questions at any time
Please share your site experiences during discussions
Respect others when they are speaking
Mobile phones on silent during the session
TRAINER INTRODUCTION & HOUSE RULES

## Slide 5: HPWJ – WATER JETTING
High pressure water jetting uses a pump to move large volumes of water through a small nozzle.
The nozzle creates the cutting or cleaning force.
Pressures commonly reach 10,000 to 20,000 psi on Anabeeb work.
It is used for surface cleaning, tube cleaning, pipe cleaning and more during shutdowns and maintenance.
KEY PRINCIPLE
The pump moves the water. The nozzle turns that flow into extreme force. This is a controlled cutting tool – not just cleaning equipment.
WHAT IS HIGH PRESSURE WATER JETTING?

## Slide 6: HPWJ – WATER JETTING
Common applications on Anabeeb and client sites:
Heat exchanger and bundle cleaning
Pipe and line cleaning
Surface preparation before coating
Vessel and tank cleaning
This work is always part of shutdown and turnaround activities. Strict controls are required every time.
WHERE HPWJ IS USED ON OUR SITES

## Slide 7: HPWJ – WATER JETTING
Waterjet injuries are different from normal cuts or bruises.
Even a small external wound can hide severe internal damage.
Medical attention is required for ALL suspected waterjet injuries – no exceptions.
The Medical Alert Card tells medical staff exactly what to look for and what treatment is needed.
It can save your life.
NEVER assume an injury is minor. Always treat every suspected waterjet injury as serious.
WHY WATERJET INJURIES ARE DIFFERENT

## Slide 8: HPWJ – WATER JETTING
Water-Cut – direct injection of water into the body
Water-Burst – sudden high-velocity burst penetrating tissue
Struck-By – hose, tool or debris hitting the body
All three must be treated seriously – the Medical Alert Card covers all types.
TYPES OF WATERJET INJURY

## Slide 9: HPWJ – WATER JETTING
Real incidents have happened in the industry:
Hose failure causing struck-by injury
Jet cutting through PPE and causing internal damage
Delayed medical treatment because the injury looked minor
LESSON
Proper controls, pre-use inspection and immediate medical response save lives. We study these incidents so we never repeat them.
REAL INCIDENT EXAMPLES – NEVER AGAIN

## Slide 10: HPWJ – WATER JETTING
Issued today – you must carry it on every high pressure water jetting job.
Waterproof and easy to access.
Tells medical staff exactly what treatment is needed.
External appearance cannot predict internal damage.
This is a mandatory safety requirement – not optional.
From this moment you are never allowed on a HPWJ job without this card in your possession.
THE MEDICAL ALERT CARD – YOUR LIFELINE
Waterjet Medical Alert Card – physician note (English & Arabic)

## Slide 11: HPWJ – WATER JETTING
Trainer will now issue one Medical Alert Card to each participant.
Sign the training roster to confirm receipt and understanding
Read the card aloud together
Photograph each participant holding their card for records
From this moment the card must be with you on every HPWJ job. It is your responsibility.
ACTIVITY – ISSUE MEDICAL ALERT CARDS

## Slide 12: HPWJ – WATER JETTING
We always apply the hierarchy of controls:
Elimination / Substitution – remove the hazard where possible
Engineering Controls – automation, mechanised systems, guards
Administrative Controls – permits, JSA, procedures, training
PPE – last line of defence, never the only control
Safer automated or mechanised methods are always preferred where reasonably practicable.
HIERARCHY OF CONTROLS
1 · Elimination / Substitution
2 · Engineering Controls
3 · Administrative Controls
4 · PPE
Most effective at the top – PPE is the last line of defence

## Slide 13: HPWJ – WATER JETTING
On Anabeeb and client sites we require:
Valid permit-to-work before any pressurised work
Job Safety Analysis (JSA) completed and reviewed by the team
Buddy system – no lone working allowed
Proper barricading and exclusion zones (minimum safe distance)
Heat stress controls and work-rest rotation
These are mandatory requirements – not optional.
KEY SITE SAFETY REQUIREMENTS

## Slide 14: HPWJ – WATER JETTING
Temporary barricades must be erected before any pressurised work.
Minimum safe distance follows industry best practice (typically 6 metres in all directions).
Use red barricade tape with clear “DANGER – HIGH PRESSURE WATER JETTING IN PROGRESS” signage.
Only authorised personnel inside the barricaded area.
If full distance cannot be achieved, additional controls (shrouds, shielding) must be used.
Never start work without proper barricading.
BARRICADING AND EXCLUSION ZONES

## Slide 15: HPWJ – WATER JETTING
KSA weather can be extremely hot. Heat stress is a real hazard during HPWJ work.
Mandatory work-rest regimen and rotation of duties.
Watch each other for early signs of heat exhaustion.
Use hydration stations and shaded rest areas.
On practical days we rotate frequently to keep everyone safe.
Safety includes looking after each other in the heat.
HEAT STRESS & WORK ROTATION

## Slide 16: HPWJ – WATER JETTING
The pump moves (displaces) water – it does not create pressure by itself.
Pressure is created only when the flow is restricted at the nozzle.
Higher pressure with a smaller orifice gives greater cutting power but also greater reaction force on the operator.
KEY RULE
The nozzle operator must always have control of the pressure relief. Know exactly where the water is going at all times.
SYSTEM FUNDAMENTALS – PRESSURE VS FLOW

## Slide 17: HPWJ – WATER JETTING
Different pressure relief control styles exist on site (standard dump, pneumatic, electrical).
The nozzle operator must always have positive control of the pressure relief method.
Different styles may add extra steps but never change the safety sequence.
Never start work if you do not fully understand and control the relief system on the equipment you are using.
PRESSURE RELIEF CONTROL & OPERATOR RESPONSIBILITY

## Slide 18: HPWJ – WATER JETTING
You have the authority and the duty to stop work if conditions are unsafe.
Stop work if:
Equipment is not properly inspected or barricaded
You are unsure about any control or procedure
Heat stress or fatigue is affecting the team
Any team member raises a concern
There is no penalty for stopping work for safety reasons. Use your SWA – it protects you and your team.
STOP WORK AUTHORITY (SWA)

## Slide 19: HPWJ – WATER JETTING
Key points from today:
Waterjet injuries can be severe even when they look minor – always use the Medical Alert Card
Follow the hierarchy of controls – safer methods first
Mandatory controls: PTW, JSA, buddy system, barricading, heat stress rotation
The nozzle operator must control pressure relief
You have Stop Work Authority – use it
Tomorrow: Equipment, Pre-Use Inspection, PPE and Job Planning + practical work with the long-barrel gun.
DAY 1 SUMMARY & KEY TAKEAWAYS

## Slide 20
END-TO-END SOLUTIONS
High Pressure Water Jetting
Basic Operator Training
(Awareness & Field Verification)
Day 2 – Equipment, Pre-Use Inspection, PPE & Long Barrel Gun Practical
Anabeeb HSE & Training | NEBOSH Verified Programme

## Slide 21: HPWJ – WATER JETTING
By the end of today you will be able to:
Identify all major components of a diesel-driven triplex HP pump and the long-barrel gun system
Perform a complete pre-use inspection of pump, hoses, fittings, whip-checks, gun and PPE
Correctly line-up, air-bleed, start-up and shut-down the system following the approved sequence
Demonstrate safe long-barrel gun stance, trigger control, reaction-force management and hand-signal communication
Complete the Day 2 practical competency checklist to the required standard
DAY 2 LEARNING OUTCOMES

## Slide 22: HPWJ – WATER JETTING
A High-Pressure (HP) Pump is a positive displacement pump designed to convert mechanical energy from a diesel engine into high-pressure water.
The pump delivers water at pressures ranging from 10,000 psi (690 bar) to 20,000 psi (1,379 bar) or higher.
It is used for industrial cleaning applications during shutdowns and maintenance.
INTRODUCTION TO THE HIGH-PRESSURE PUMP

## Slide 23: HPWJ – WATER JETTING
Power Unit (Diesel Engine) – Drives the pump
Triplex Plunger Pump – Produces high-pressure water
Plungers – Compress water to high pressure
Suction & Discharge Valves – Control water flow
Pressure Regulator / Unloader Valve – Controls operating pressure
Pressure Relief Valve – Prevents over-pressure
Pressure Gauge – Displays operating pressure
Emergency Stop Button – Immediately shuts down the system
MAIN PARTS OF AN HP PUMP

## Slide 24: HPWJ – WATER JETTING
Before operating the HP pump, perform the following inspections:
Barricades installed and signage in place
Engine oil level correct
Pump oil level correct
Fuel level adequate
Cooling system condition good
Battery condition good
Belts and couplings in good condition
No oil or water leaks
Pressure gauge calibrated
Emergency stop button functional
Safety relief valve installed and operational
Never start the pump until all pre-start checks are complete and satisfactory.
PRE-START INSPECTION OF THE HP PUMP

## Slide 25: HPWJ – WATER JETTING
Before use, inspect all high-pressure hoses:
Correct pressure rating for the job
No cuts, abrasions or damage to the outer cover
No bulges or soft spots
No damaged or leaking fittings
Safety whip checks installed and in good condition
Hose restraints installed where required
Hose routed safely with no kinks or sharp bends
Never use a damaged or suspect hose. Replace immediately.
HP HOSE INSPECTION

## Slide 26: HPWJ – WATER JETTING
Before use, inspect the gun and accessories:
Trigger functioning smoothly
Trigger guard in place and undamaged
Safety latch / lock working correctly
Correct nozzle fitted and secure
Lance straight and undamaged
All connections tight
GUN / TOOL INSPECTION

## Slide 27: HPWJ – WATER JETTING
The following PPE is mandatory for high pressure water jetting work:
Safety helmet with face shield
Safety goggles
Hearing protection
TST water jetting suit (correct rating)
Cut-resistant gloves
Steel-toe safety boots
Waterproof clothing where required
TST suits are the primary protection against high-pressure water jet injuries.
REQUIRED PPE FOR HPWJ

## Slide 28: HPWJ – WATER JETTING
TST suits are specially designed multi-layer protective suits for high-pressure water jetting.
They are engineered to protect against water jet penetration up to the rated pressure.
The suit consists of an outer protective layer and inner protective layers that work together to deflect and absorb high-pressure water.
TST suits are the most important piece of PPE when working with high-pressure water jetting equipment.
A TST suit is your last line of defence against serious injury.
WHAT IS A TST SUIT?

## Slide 29: HPWJ – WATER JETTING
TST suits typically include:
Outer protective layer (high-strength fabric)
Inner protective layers (designed to deflect water jets)
Reinforced areas at high-risk zones (arms, torso, legs)
Sealed cuffs and neck protection
Different protection ratings (e.g. 500 bar, 1000 bar, 2000 bar)
Always use a suit with the correct pressure rating for the equipment being used.
Never use a TST suit below the required pressure rating for the job.
COMPONENTS & PROTECTION LEVELS OF TST SUITS